For Both Robot & Workstation
connect to the same wifi network

For Robot:
- open .bashrc file
  - #export ROS_MASTER_URI = http://localhost::11311
  - #export ROS_HOSTNAME=[robot ip address]
- run command <<roslaunch turtlebot_bringup minimal.launch>>

For Workstation:
- to determine workstation IP address
  - use command <<ifconfig>>
- open .bashrc file
  - add the following lines
    - export ROS_MASTER_URI= [robot ip address]
    - llllexport ROS_HOSTNAME= [workstation ip address]
      - Turtlebot 1 IP Address: 192.168.42.149:11311
      - Turtlebot 2 IP Address: 192.168.42.214:11311
      - Turtlebot 3 IP Address:
- to connect to robot
  - use command <<ssh turtlebot@[robot ip address]

To Pull A Repository from Github:
- mkdir -p ~/catkin_ws/src/[folder name]
- cd ~/catkin_ws/src/[folder name]
- git init
- git pull [github address]

Minimal Turtlebot Launch:
- <<roslaunch turtlebot_bringup minimal.launch>>
- <<roslaunch turtlebot_teleop keyboard_teleop.launch>>

Camera Launch Bringup:
- <<roslaunch openni_launch openni.launch>>
- <<roslaunch turtlebot_bringup 3dsensor.launch>>

Gmapping:
- <<roslaunch turtlebot_bringup minimal.launch><
- <<roslaunch turtlebot_navigation gmapping_demo.launch>>
- <<roslaunch turtlebot_rviz_launchers view_navigation.launch>
- <<roslaunch turtlebot_teleop keyboard_teleop.launch>>

once mapping is finished, save map

rosrun map_server map_saver -f [map location]

AMCL:
- roslaunch turtlebot_bringup minimal.launch
- roslaunch turtlebot_navigation amcl_demo.launch map_file:=
- roslaunch turtlebot_rviz_launchers view_navigation.launch